## Slide 1
SRAN Sales Playbook
V7.0
October 2017

## Slide 2
1
2
3
4
5
6
7
8
Executive Summary
Single RAN
Portfolio
Customer
Benefits
Sales Guidance
Pricing
CI
References
Contacts

## Slide 3
The key drivers for Single RAN
Data traffic boom continues
Gbps
race
Growing energy costs, operators setting long term sustainability targets* to reduce carbon dioxide emissions
M€
CO2
BRAND
Uncertainty in capacity life cycles
4G
3G
2G
5G
New Radio Access Network (RAN) equipment adds complexity and costs
4G
3G
3G
2G
2G
2G
CAPEX
OPEX
* http://sciencebasedtargets.org/

## Slide 4
  Simpler and more effective business
  30% lower TCO*
The future just got simpler
Single RAN Advanced – our promise
  Faster to revenue
  Simplified investment balancing
  Reduced site costs
  Smaller energy bill
  Lower backhaul costs
  Lower operation and maintenance costs
  Less spare parts
  Best performance
  Our solution consists of multipurpose hardware and common software for GSM, WCDMA and LTE technologies
  Typical use cases
  Ready for 4G revenues without site visits
  Ready for frequency re-farming without site visits
  Continue legacy radio access technologies with marginal costs
* Total Cost of Ownership compared to LTE overlay
2G LTE Base Station
3G WCDMA Base Station
4G GSM Base Station
Single RAN Base Station
GWL
LTE overlay

## Slide 5
1
2
3
4
5
6
7
8
Executive Summary
Single RAN
Portfolio
Customer
Benefits
Sales Guidance
Pricing
CI
References
Contacts

## Slide 6
The future just got simpler
Nokia Single RAN Advanced Product Portfolio
Common Software
Multipurpose Hardware
SBTS software
Flexi Multiradio 10 Base Station
Multicontroller
AirScale Active Antennas
RAS
SRAN release
SBTS
mcBSC/BSC
mcRNC/RNC/OMS
RF Sharing
Common Backhaul
S1/X2
Iub
PAbis
IP
System Module Sharing
GWL
Fronthaul Sharing
G
W
L
OBSAI
CPRI
AirScale
Base Station
Power Management
Zero emission 2.0
Power Battery, Power Rectifier, Power Prioritizer
POW
Single BTS OAM
Web UI
Application SW
FDD-LTE
TDD-LTE
WCDMA
GSM
5G
FIRST
Nokia Internal Use

## Slide 7
The future just got simpler
Single RAN Advanced Portfolio – Key Offering
Flexi System Module
Flexi RF Module
Flexi Power
SBTS Software
SRAN Release
AirScale Active Antennas
AirScale Remote Radio Head
OneClip
AirScale System Module
Multicontroller BSC/RNC
Flexi Cabinets
AirScale Outdoor Cabinets
Nokia Internal Use

## Slide 8
Boost your network performance
SRAN17A: Our next SRAN release
Nokia Internal Use
New cell set concept for considerably faster site roll-out
Improved security
Increased resource sharing
New BTS O&M architecture reducing work load
Huge number of added value LTE, WCDMA and GSM features
Improved backhaul transport
AirScale Indoor System Module support
New radios supported

## Slide 9: Nokia AirScale Base Station Platform
Efficiently enriching user experience
Nokia AirScale
System
Module
Multiband radios – including World’s first Triple band radio
  System module chaining
  Highly resilient and redundant
  Zero Emission
5 RAT, 4.5G Pro, 4.9G, 5G & Cloud enhanced
  28 Gbps capacity per system module
Highest possible availability
Power meter, control and management for greener world
5G, LTE, TD-LTE, WCDMA, GSM configurations
Unlimited capacity and connectivity
Ultra lean and efficient sites
One stop shop
Nokia AirScale
Radio
5G
FIRST
Nokia Internal Use
Notes: This slideset does not cover AirScale Acitve Antennas

## Slide 10
AirScale System module – High Capacity (Indoor & Outdoor)
AMIA with PIUs equipped
Indoor
128x447x400 mm
-5 to +60 deg
High IP throughput
High capacity
Colossal RF bandwidth
High backplane connectivity
4 RAT site solution
Indoor & outdoor subracks
2TB
7.68 GHz
IP20 AMIA
IP55 AMOB
10 Gbps
Common SW
LTE 96 cells
WCDMA 48 cells GSM 36 TRXs
AMOB with PIUs equipped
Outdoor
355x487x605 mm
-40 to +55 deg
Based on SRAN17A configurations
Nokia Internal Use
Note: Airscale full rack support will be available with SRAN17A MP1
Notes: For AMIA: Temperature range -5°C to +60°C (front to back), Temperature range -5°C to +55°C (back to front)
AMIA is 3U, AMOB is 8U high

## Slide 11
Flexi Multiradio 10 Base Station – Product highlights
Software-defined base station
One, two or three radios concurrently
LTE SW
Up to 18x20MHz@2x2MIMO
GSM SW
Up to 36 TRX
WCDMA SW
Up to 24x5 MHz
Easy baseband capacity expansion
Core Module
Core Module
Extension
Extension
Extension
Extension
3-sector RF module
1
2
3
3 pipe/ 3T6R
6 pipe/ 6T6R
1
2
3
WCDMA
FSMF: GSM&WCDMA
LTE
Opt. PDU
Opt.TRS ext
WCDMA
GSM&WCDMA
WCDMA
LTE
LTE
LTE
Opt. PDU
Opt.TRS ext
Opt. PDU
Opt.TRS ext
Note: 2x FSMF support will be available with SRAN17A MP1

## Slide 12
Flexi Multiradio 10 System Module
Flexi Multiradio 10 Base Station
In volume deliveries
Flexi Power Rectifier
Flexi Power Battery
Flexi RF Module
Flexi Remote Radio Head
Flexi Radio Antenna Solution

## Slide 13
FCOB
Flexi Cabinet Outdoor
8,5U
Cabinet and casing options
AirScale system module can be installed also to Flexi cabinets
FCOA
Flexi Cabinet Outdoor
40U
FCIA
Flexi Cabinet Indoor
  36U
AMOB
AirScale Cabinet Outdoor
8U

## Slide 14
Adding equipment to legacy sites increases energy bill and CO2 emissions
Turn the zero carbon vision into business opportunity
Zero Emission 3.0 Offering
Modernized zero carbon sites for better business
Rectifier
GSM BTS
Air con
Battery
WCDMA BTS
LTE BTS
Typical modernization payback in 2-3 years; Zero carbon sites by renewable energy
AirScale BTS
Rectifier
Battery
Energy Efficiency Software Features
Embedded Power Metering
Micro DTX Extension
SIMO to MIMO SW
RF layer switch-off SW
Enhanced BCCH TRX energy saving
Static power management
Radio load based dynamic power management
Power saving with radio module shutdown
Assett Recovery & Re-marketing
kW
€
Eden-NET
Energy Management
Hybrid trunk
AirScale Active Antenna
Renewable energy

## Slide 15
Single RAN services – addressing all use cases
Fast deployment, managed complexity, minimized risk, best performance, minimized TCO
Benefits for our customers
Best performance with Nokia’s network design and optimization services
Fastest time-to-market, lowest risk and complexity with Nokia’s deployment services
Minimized TCO with optimal re-use of site assets
E2E Service Offerings
Design
Deployment
Performance
Care
Network Design for modernization
Network Design for re-farming
Network deployment for modernization
Network Cloning
Energy Solutions
Network Optimization
Multi-layer Optimization
Hardware Services
Software Services
Asset recovery and take-back
Available Services:
Multi-layer optimization
Site solution catalogs and new model sites
Site engineering service with twice the experience & capabilities
“We delivered our nationwide 4G LTE network months ahead of schedule, thanks in part to the strong partnership and expert support of Nokia. What’s more, our nationwide 4G LTE network is the fastest in the US, which translates to a great experience for all of our data-hungry customers.”
Neville Ray, Chief Technology Officer, T-Mobile USA

## Slide 16
NetAct - Overview & Role in Single RAN Approach for true SRAN operations
  Reduce used time for searching and visualization
  Search Single RAN BTS site as one entity
  Simplify Single RAN BTS configuration setup
  Operations for Single RAN level instead of individual RATs
  Monitoring
  Investigate failures and impacts on Single RAN level
  Configuration and Software Management
  Changes to whole BTS as one single operation
  View SW configuration of whole Single RAN BTS
OSS
OSS
SRAN network
NetAct
NetAct
NetAct
WCDMA
GSM
LTE
GSM
WCDMA
LTE
NetAct
Note: NetAct supports multi-RAT already
Including RNC and BSC
Umbrella / 3rd party
BTS Mediator
Notes: Network operations is transforming from vendor /technology centric approach to area centric approach. In the slide from left to right, there are there are four areas where Single RAN has an impact:
How the network is operated
For example, there can be Radio Access Technology (RAT) specific teams in operations center vs. teams per certain geographical area handling all technologies.
This is a major change to operators; Mobile networks have always been managed in a very network element driven manner. Experts operating base stations must know all the details of that particular equipment and technology to be able to operate base stations which will then form a network.
When new technologies (for example WCDMA) came, there were new experts who familiarized themselves with the new technology and then operated that new group of network elements. They had to agree with GSM experts how to manage adjacencies. So the intelligence to manage a mixed network resided in operators’ heads and not in the system itself.
Although LTE is simpler to operate than WCDMA, it still increases the complexity of the network when LTE is placed on top of existing WCDMA and/or GSM network. So it’s not feasible keep on add ing layers to network operations and layers to network operating personnel and manage network elements as individual boxes.
Separate OSS systems for different technologies vs. common multi-technology OSS system
A natural requirement for a unified way of operating the network is to have an OSS system that can support the new process. As there are typically lots of integrations and in-house tools in the OSS layer, all those need to be planned and implemented. It’s is a big project that must be planned carefully.
Radio network seen as one vs. loosely coupled separate radio access technologies
After step one and two, network can be seen as “one” - having different capabilities, for example, different technologies, different layers which are optimized for used services
Network is not anymore a group of individually or manually configured base stations
Optimization target is to create a network which works optimally as a whole, not only for one technology or one type of base station
Base station is managed as one Single RAN base station vs. strong technology driven management
Base station is seen as ”router” for traffic
Operator can truly manage OPEX and CAPEX of the whole radio network - not just per technology
Also services can be configured to be good enough in certain area but not on the same level to all WCDMA areas in the whole network.
- Single RAN requires a common OSS solution and operations approach to realize the OPEX benefits, and operability is an important part of the solution
- There are also related up-sell opportunities beyond Single RAN within CEM and OSS

## Slide 17
New Element Management Tool
IMI
IMI
NetAct
Data
Center
Web UI
Element Management Tool
NE3S
SBTS OAM
NE3S
SRAN 16.x
SRAN 17A
Common O&M
Common Transport
GSM application
FDD LTE application
WCDMA application
SBTS
GSM application
FDD LTE application
WCDMA application
SBTS
Single BTS O&M code w/ unified object model
SRAN from SRAN 16.10 to SRAN 17A
REST
Common Transport
BTS
Mediator
NetAct Data Center
NetAct
NE3S
  Reducing time spent on searching and visualization
  Search Single RAN BTS site as one entity
  Simplify Single RAN BTS configuration setup
  Operations for Single RAN level instead of individual RATs
Multi BTS connection to mediator possible
Nokia Internal Use

## Slide 18
“Single BTS O&M” is more than the BTS SW code. “Single BTS O&M” consists of four components
Single BTS O&M code in SBTS/eNB based on LTE
Common Transport code in SBTS/eNB based on SRAN
New Element Management tool replacing both WebUI from SRAN 16.x as well as Site Manager
New BTS Mediator
Single BTS O&M Components
New Element Management Tool
BTS Mediator
GSM application
FDD LTE application
WCDMA application
BTS / eNB
TD LTE application
BTS Mediator
New Element Management Tool
IMI
IMI
Single BTS O&M code w/ unified object model
Single BTS O&M code w/ unified object model
NBI
Data structure in NetAct northbound interface will change. This will have impact on the existing integrations with higher level management systems.
NetAct dimensioning rules will change.
Common Transport
Common Transport
NetAct Data Center
NE3S
NetAct
IMI – InfoModel Interface
NBI – Northbound Interface
Nokia Internal Use
Notes: Data structure in NetAct northbound interface will change.
-> This will have impact on the existing integrations with higher level management systems
-> and also all customization support (including scripts, etc. ) based on previous object model needs to adapt the changes
NetAct dimensioning rules will change.

## Slide 19
SRAN 17A Overview
Common BTS OAM
Common handling in NetAct, Simplified site creation, commissioning and configuration
Web UI for local management:
Minimize care/O&M efforts with
no specific tools to connect SBTS
New SBTS Software
  Combine one base station for GSM, WCDMA and LTE radio technologies
  Flexi Multiradio 10
  Introduction of AirScale Base stations
    System module sharing
    Extremely compact sites
    Lower energy consumption
    Scalable capacity
Common backhaul IP transport
    One IP host and interface
    One IP address and IP security
    No external IP transport boxes
GWL
Nokia Internal Use

## Slide 20
SRAN17A architecture
  SRAN17A architecture is different than in SRAN16.2/16.10
  SRAN17A architecture is based on LTE architecture and a new BTS mediator adaptation layer is presented.
Site visit
  WCDMA BTS (FSMF) and LTE BTS (FSMF) can be migrated to SBTS (FSMF) architecture without a site visit.
  GSM BTS (FSMF) requires a site visit, because RFS tool cannot be used remotely.
  If several technologies are combined to same SBTS this requires e.g. physical cable changes to SBTS and it requires a site visit.
  If HW type is changed it always requires a site visit
Backward compatibility
  NetAct, WCDMA OMS and Controllers (BSC and RNC) provides backward compatibility from top to down direction.
  This means that before SBTS17A migration the NetAct, WCDMA OMS and Controllers needs to be in SRAN17 level if all of those technologies are used.
RAT migration to SRAN17A architecture
NetAct
Data center
SBTS 17A
(GSM, WCDMA
and LTE RATs)
NetAct 17.8
BTS Mediator
RNC17
BSC17
WCDMA OMS 17
WBTS17
<optional>
GSM BTS17
<optional>
eNB17
<optional>
LTE OMS 17* <optional>
BTS EM
* iOMS is not needed for LTE in SBTS
Nokia Internal Use

## Slide 21
NetAct
Data center
NetAct is upgraded to NetAct 17.8 SP level
New BTS Mediator with SRAN 17A SW is deployed to NetAct Data Center
OMSs are upgraded to WCDMA OMS17 and (Optional: LTE OMS17 level)
Controllers are upgraded to WCDMA 17 / GSM 17 level
BTS RAT Migration to SBTS17A
  One or several radio technologies (LTE, WCDMA or/and GSM) are migrated to SBTS17A
Upgrade to SRAN17A
  6.1 <Optional> upgrade for traditional BTSs (LTE, WCDMA and GSM)
  e.g. If BTS HW is not supported for SRAN architecture the existing BTSs can be kept in the traditional architecture
  6.2 <Optional> upgrade for SBTs from SRAN16.x to SRAN17A. It doesn’t require site visit.
Migration steps in high level
SBTS 17A
(GSM, WCDMA
and LTE RATs)
NetAct 17.8
BTS Mediator
NE3S
SOAM IF
RNC17
BSC17
NWI3
Q3
BTS OM
WCDMA OMS 17
WBTS17
<optional>
GSM BTS17
<optional>
eNB17
<optional>
LTE OMS 17 <optional>
BTS OM
NWI3
BTS OM
BTS EM
Abis
SCF
SOAM Info Model
SCF
SCF
SCF
* iOMS is not needed for LTE in SBTS
Nokia Internal Use

## Slide 22
SON - automated manner to optimize network
NetAct functionality for SRAN
BTS Site Manager
“not commissioned”
Repeat PnP
Nokia Auto Configuration
Use case 1: no DHCP server in operators network, but auto- configuration is available
Local configured
PnP transport
parameters
Start auto-configuration
Use case 2: eNB commissioned PnP shall be repeated
Clear
PnP state
BTS Site Manager
  SON assists operators to autonomously optimize their Single RAN network, to improve network performance and customer experience.
    The logic is the same in SRAN with SBTS as in traditional radio network with SRAT BTS
    Single RAN specific SON features include
      Automated Site Creation with Plug and Play
      Minimize drive test
      Energy Saving solution
    Single RAN BTS has own set of configuration parameters
      SON optimizes the network parameters
      NetAct Configurator manages the network parameters (provisioning changes, mass editing, auditing etc)

## Slide 23
SRAN SW Compatibility Plan
SRAN16.10 SW Component | SRAN SW Compatibility
SBTS16 | SBST 16.10
WBTS16 | WBTS 16.3
WCDMA16 | WCDMA 16.3
GF16 | GF 16.5 1.0
GSM16 | GSM16 3.0
FL16 | FL16 6.0
NetAct | NetAct 16.5 + INES SP
NetAct 16.5 SW package | Delivery schedule
NetAct 16.5 P7 SW | Mid of May (M 05/16)
NetAct 16.5 C5 SW | End of June (E 06/16)
NetAct 16.5 Open Stack SW delivery for MCCI Iran | Mid of July (M 07/16)
NetAct 16.5 INES SP SW - supporting SRAN16.10 P7 SW | Mid of August (M 08/16)
NetAct 16.5 INES SP SW update -requried for SRAN16.10 P8/C5 SW | End of October (E 10/16)
OSS NetAct version for SRAN 16.10 release support
SRAN SW Release Compatibility
SRAN17A SW Component | SRAN SW Compatibility
SBTS17 | SBTS17A
WBTS17 | WBTS17 3.0
WCDMA 17 | WCDMA 17 MP2 (RNC17 2.0)
GF17 | GF17 2.0
GSM 17 | GSM 17 MP2 (BSC17 2.0)
FL17, FL17 SP | FL17A
NetAct | NetAct 17.8 + SP
NetAct 17.8 SW package | Delivery schedule
NetAct 17.8 SP1710 PT (SRAN 17A PT) | M10/17
NetAct 17.8 SP1710 P8 (SRAN 17A P7) | E10/17
NetAct 17.8 SP1712 P8 (SRAN 17A P8) | E12/17
Nokia Internal Use

## Slide 24
1
2
3
4
5
6
7
8
Executive Summary
Single RAN
Portfolio
Customer
Benefits
Sales Guidance
Pricing
CI
References
Contacts

## Slide 25
Example: cost components of a medium capacity site
Value of Nokia SRAN: lower TCO especially from OPEX reduction
Site rental
23%
Power consumption
11%
Transmission OPEX
9%
4%
OAM
12%
SW
8%
Total site cost
-100%
Radio
27%
3%
Transmission CAPEX
Antenna line
NI&Power
3%
Site OPEX 70%
Site CAPEX 30%
Nokia SRAN benefits
Lower site rent
Simpler maintenance
Lower power consumption
Less installation effort
Smaller battery bank
Less transmission equipment
Simpler antenna line, less RF fibre
€€€

## Slide 26
Key Hunan Unicom benefits
Re-use of 2G and 3G base station HW and sites
4G LTE launch one month earlier
48% CAPEX savings
80% OPEX savings
Multi million euro annual savings
While maintaining high quality 2G/3G service level
Hunan Province
68M people
2,5B€ Internet Plus program
LTE subscribers doubled
3.8 times data traffic
First in China to deploy Single RAN software
Hunan Unicom
Ms. Yu Yuequn,
Senior Technical Manager and DGM
Unicom Changsha branch
Key costs saving contributors
    CAPEX (HW)
    Energy
    Backhaul
    Work
    Site costs
Chart: 
| CAPEX (HW) | Energy | Backhaul TRS | Work | Site cost
Savings | 5000 | 2700 | 1000 | 700 | 12000
”How to hit our 4G ambition while reducing network complexity ?
Nokia Single RAN enabled rapid, average one day 4G upgrade to existing BTS sites reducing needed antennas, shelters, tower costs while also reducing energy costs”
Single RAN Advanced – Hunan Unicom, China
4G roll-out with 80% lower OPEX

## Slide 27
2 cabinets & 12 radios , 3 separate basebands
GSM with TDM; IP for WCDMA and LTE
SRAN SW Relese, 4 radios,
common baseband, O&M and TRS, all-IP
SRAN Benefit: reducing site complexity

## Slide 28
Single RAN Benefit: common SW delivery
GSM SW
GSM Application
GSM O&M
GSM Transport
FD LTE SW
FD LTE Application
FD LTE O&M
FD LTE Transport
WCDMA SW
WCDMA Application
WCDMA O&M
WCDMA Transport
GSM Application
WCDMA Application
FD LTE Application
Common BTS O&M
Common Transport
Common SBTS SW:
Dedicated SW Packages

## Slide 29
Flexi Multiradio 10 BTS: System Module Sharing single-RAT mode
WCDMA
WCDMA
WCDMA
Opt. PDU
Opt.TRS ext
System Module Rel.3 | Capacity Extension Submodule | Number of Subunits
FSMF | - | 5.5
FSMF | FBBA/C | 11.5
FSMF | 2xFBBA/C | 17.5
For details check Dimensioning WCDMA RAN: Flexi BTS Baseband
There is no one way to describe WCDMA capacity in SBTS (as in WCDMA)
WCDMA capacity depends on many factors like
Common Control Channel (CCCH) dimensioning with 1-4 Local Cell Groups
2-Way RX Diversity
cell range
Rel.99 vs. HSDPA vs. HSUPA capacity allocation
Parallel Interference Cancellation (PIC)
DC-HSDPA and DB-HSDPA
Local Cell Grouping
All WCDMA subunit figures are based on 1 Local Cell Group and R99 traffic only
Nokia Internal Use

## Slide 30
Flexi Multiradio 10 BTS: System Module Sharing 2-RAT modes
WCDMA
GSM&WCDMA
WCDMA
LTE
GSM&LTE
LTE
Opt. PDU
Opt.TRS ext
Opt. PDU
Opt.TRS ext
System Module Rel.3 | Capacity Extension Submodule | WCDMA BB: No. of Subunits | GSM BB
FSMF | - | 3.5 | 24 TRX
FSMF | FBBA/C | 9.5 | 24 TRX
FSMF | 2xFBBA/C | 15.5 | 24 TRX
FSMF | 2xFBBA/C | 14.5 | 36 TRX
System Module Rel.3 | Capacity Extension Submodule | LTE BB | GSM BB
FSMF | - | RCS | 24 TRX
FSMF | FBBC | RCS + BCS | 24 TRX
FSMF | 2xFBBC | RCS + 2x BCS | 24 TRX
FSMF | 2xFBBC | RCS + ECS | 24 TRX
Reduced cell set (RCS)
up to 3x10MHz LTE 2x2 MIMO with CoMP in FSMF
up to 4x10MHz LTE 2x2 MIMO without CoMP in FSMF
BCS=basic cell set, ECS=extended cell set, RCS=reduced cell set
Nokia Internal Use

## Slide 31
Flexi Multiradio 10 BTS: System Module Sharing 2-RAT modes
LTE
LTE
WCDMA
Opt. PDU
Opt.TRS ext
WCDMA
WCDMA
LTE
Opt. PDU
Opt.TRS ext
WCDMA
FSMF: WCDMA
Opt. PDU
Opt.TRS ext
LTE
FSMF: LTE
LTE
Opt. PDU
WCDMA
System Module Rel.3 | Capacity Extension Submodule | WCDMA BB: No. of Subunits | LTE BB
FSMF | 2xFBBC | 5.5 | 2 x BCS
FSMF | 2xFBBC | 5.5 | 1 x ECS
System Module Rel.3 | Capacity Extension Submodule | WCDMA BB: No. of Subunits | LTE BB
FSMF | 2xFBBA/C | 11.5 | 1 x BCS
System Module Rel.3 | Capacity Extension Submodule | WCDMA BB: No. of Subunits | LTE BB
2xFSMF | 4xFBBA/C | 17.5 | 3 x BCS
2xFSMF | 4xFBBA/C | 17.5 | 1 x ECS + 1 x BCS
BCS=basic cell set, ECS=extended cell set, RCS=reduced cell set
Nokia Internal Use
Note: 2x FSMF support will be available with SRAN17A MP1

## Slide 32
Flexi Multiradio 10 BTS: System Module Sharing 3-RAT modes
WCDMA
FSMF: GSM&WCDMA
LTE
Opt. PDU
Opt.TRS ext
WCDMA
FSMF: GSM&WCDMA
Opt. PDU
Opt.TRS ext
LTE
FSMF: LTE
LTE
Opt. PDU
WCDMA
WCDMA
FSMF: GSM&LTE
WCDMA
Opt. PDU
Opt.TRS ext
System Module Rel.3 | Capacity Extension Submodule | WCDMA BB: No. of Subunits | LTE BB | GSM BB
FSMF | 2xFBBA/C | 11.5 | 1 x RCS | 24 TRX
System Module Rel.3 | Capacity Extension Submodule | WCDMA BB: No. of Subunits | LTE BB | GSM BB
FSMF | 2xFBBA/C | 9.5 | 1 x BCS | 24 TRX
FSMF | 2xFBBA/C | 8.5 | 1 x BCS | 36 TRX
System Module Rel.3 | Capacity Extension Submodule | WCDMA BB: No. of Subunits | LTE BB | GSM BB
2xFSMF | 4xFBBA/C | 15.5 | 3 x BCS | 24 TRX
2xFSMF | 4xFBBA/C | 14.5 | 3 x BCS | 36 TRX
2xFSMF | 4xFBBA/C | 15.5 | 1 x BCS + 1 x ECS | 24 TRX
2xFSMF | 4xFBBA/C | 14.5 | 1 x BCS + 1 x ECS | 36 TRX
BCS=basic cell set, ECS=extended cell set, RCS=reduced cell set
Nokia Internal Use
Note: 2x FSMF support will be available with SRAN17A MP1

## Slide 33
AirScale System Module - SRAN
The AirScale System Module is built of:
one subrack: AMIA AirScale Subrack
One sub-rack fits one or two independent logical SBTSs consisting of
one or two core modules ASIA AirScale Common
minimum one, maximum six capacity extension modules ABIA AirScale Capacity
Each ABIA can be used for allocation of LTE or SRAN cell sets
one logical SBTS
ABIA
ASIA
ABIA
ABIA
ABIA
ASIA
ABIA
ABIA
one logical SBTS
LTE TDD eNB
Subrack
Half subrack
Half subrack
3 U
ASIA Common
Common unit
Control Plane
Transport connectivity
AMIA Subrack
housing for ABIA and ASIA plug-ins
Backplane interconnections between cards
ABIA Capacity
Baseband plug-in
User Plane
RFM connectivity
ABIA
AirScale
Baseband
Indoor
ASIA
S - Core or Common functions
AMIA
M - Subrack
Note: Airscale full rack support will be available with SRAN17A MP1

## Slide 34
SBTS
AirScale BB dimensioning
SBTS follows dedicated LTE BB dimensioning:
Basic Cell Set
Extended Cell Set
XL Cell Set
Packed Cell Set
Dual-Packed Cell Set
NB-IoT dimensioning rules
SRAN WCDMA BB dimensioning calculated based on available #SU (similar as FSMF)
One ABIA equals to 8 SU
GSM dimensioning presented in #TRXs
LTE
WCDMA
GSM

## Slide 35
LTE Cell set mapping to AirScale System Module
Up to two basic cell sets per module:
both cell sets share 6 ports
With this feature one cell set can utilize max 4 ports, leaving 2 ports left for the other
One extended cell set per module:
up to 6 ports can be used
configurations in extended cell set are mainly defined to allow ULCoMP and SuperCell between cells
ABIA
Basic cell set:
for 2 Antennas (2Tx/2Rx):
3 cells @ 15/20MHz
or
2 cells @ 5/10MHz + 2 cells @ 15/20MHz
or
4 cells @ 5/10MHz
for 4 Antennas (4Tx/4Rx or 2Tx/4Rx):
2 cells @ 5/10/15/20MHz
Basic cell set:
for 2 Antennas (2Tx/2Rx):
3 cells @ 15/20MHz
or
2 cells @ 5/10MHz + 2 cells @ 15/20MHz
or
4 cells @ 5/10MHz
for 4 Antennas (4Tx/4Rx or 2Tx/4Rx):
2 cells @ 5/10/15/20MHz
ABIA
Extended cell set:
for 2 Antennas (2Tx/2Rx):
6 cells @ 5/10/15/20 MHz
for 4 Antennas (4Tx/4Rx or 2Tx/4Rx):
3 cells @ 5/10/15/20MHz

## Slide 36
LTE Cell set mapping to AirScale System Module
ABIA
packed cell set:
for 2 Antennas (2Tx/2Rx, 2x2 MIMO):
6 cells @ 20MHz
or
8 cells @ 10MHz / 20MHz mixed*)
for 4 Antennas (4x2 MIMO 4Rx div, 4x4 MIMO):
3 cells @ 20MHz
or
4 cells @ 10MHz / 20MHz mixed *)
Up to two packed cell sets per ABIA module:
both cell sets share 6 ports
With this feature one cell set can utilize max 4 ports, leaving 2 ports left for the other
packed cell set:
for 2 Antennas (2Tx/2Rx, 2x2 MIMO):
6 cells @ 20MHz
or
8 cells @ 10MHz / 20MHz mixed *)
for 4 Antennas (4x2 MIMO 4Rx div, 4x4 MIMO):
3 cells @ 20MHz
or
4 cells @ 10MHz / 20MHz mixed *)
ABIA
dual packed cell set
for 2 Antennas (2Tx/2Rx, 2x2 MIMO):
12 cells @ 20MHz
or
16 cells @ 10MHz / 20MHz mixed*)
for 4 Antennas (4x2 MIMO 4Rx div, 4x4 MIMO):
6 cells @ 20MHz
or
8 cells @ 10MHz / 20MHz mixed*)
One dual packed cell set per ABIA module:
up to 6 ports can be used
Contains 2 baseband pools, to provide sufficient capacity for multi-carrier and chaining configurations
UL CoMP and SuperCell possible inside each BB pool
Note about Cell numbers:
15 MHz instead of 20 MHz is supported as well
5 MHz instead of 10 MHz is supported as well
for cases with 2 Antennas, 1.4 MHz or 3 MHz cells instead of 10MHz cell are supported as well
*) In case of mixture of 10MHz and 20MHz cells, max 50% of the cells can be 20MHz
Feature LTE2733 Baseband pooling needed

## Slide 37
LTE
AirScale SRAN BB cell sets: 3-RAT sharing deployment
Nokia Internal Use
ABIA:
WCDMA
Optional BB extensions
W/G
GSM
Optional BB extension increment
W
W
W
SRAN cell set
LTE
GSM
SRAN LTE-WCDMA-GSM
sharing
LTE – as per LTE cell sets definition
GSM – 24 or 36TRX
WCDMA – 4 or 6 SU in shared ABIA
Increments of 2 SU on top of LCG
Up to 24 Wcells/ half sub-rack*
Up to 6 RF ports can be use for
shared RF units
Additional ABIA can be
added as BB pool extension
(max 3 in total within one half sub-rack)
ABIA:
Optional BB extensions
W
W
W
SRAN cell set
WCDMA
Nokia Internal Use

## Slide 38
On Transport layer site appears as one IP host
Focus on IP/ETH-based Transport modes
Single SBTS Transport feature set covering all RATs
Flexible IP addressing, QoS and IPsec concepts
Unified Transport Operability
Shared transport function in SBTS with unified operability
S1/X2
Iub
Packet
Abis
IP
Ethernet
Full packet backhaul example
SBTS
GSM
WCDMA
LTE
Common Transport
Common Transport with Single RAN BTS (SBTS) sites
SRAN Transport features replace dedicated RAT features
GSM
WCDMA
LTE
TRS-G
TRS-W
TRS-L
WCDMA
LTE
GSM
Common
Transport
SR000356 IPsec for BTS
BSS21444 Packet Abis Security
RAN1747 IPsec for BTS
LTE689 LTE IPsec Support
Nokia Internal Use
Notes: In SRAN16.2 Packet Abis over TDM interfaces are supported only for:
SBTS in GSM dedicated mode
TDM as fallback for Packet Abis over IP/Eth

## Slide 39
Combining the strengths of LTE and SRAN O&M to cater to the growing customer base base
New Single BTS O&M Architecture
SBTS O&M architecture providing scalability and faster time to market
Feedbacks from initial SBTS customers
  Profile concept in SRAN 16.x O&M architecture is too rigid, lacks scalability and flexibility
  LTE features are the key requirement in all SBTS deployments
  There is a need to have more flexibility on supported configurations to facilitate migration from Single RAT to Single RAN sites
New Single O&M Architecture for LTE and SRAN
  Static configurations (profiles) moved to dynamic LTE based configuration solution
Common O&M ensures full feature parity with latest LTE features and support of LTE configurations
  AirScale introduction can be done most efficiently on Single BTS O&M, both from efforts and from configuration point of view.
Solution
Nokia Internal Use

## Slide 40
Typical Use cases for SBTS Deployments
Competitor Installed Base Modernization with Nokia Single RAN
Own installed Base Modernization with Single RAN
Existing customer with mixed HW configurations
1
2
3

## Slide 41
Legacy 2G/3G site evolving to Single Band / Dual Band LTE
Example 1: Competitor SWAP with Nokia SRAN
GSM/ LTE1800:
G4+4+4@20W & L1+1+1@10 MHz
LTE800: 1+1+1@10 MHz
WCDMA 2100 2+2+2@20W
GSM/ WCDMA900
G3+3+3@20W & U1+1+1@20W
2G FSMF
Entry with single System module
Unique offer of 3-pipe and 6-pipe RFM
Maintaining GSM Traffic with lesser TRXs using GSM Spectral efficiency features
Simple antenna line: No combiner losses, short feeders
2G FSMF
2G/ 3G/ 4G FSMF+ 2 FBBC
2G/4G RFM FXED 1800
2G/3G RFM FXDB 900
3G RFM FRGT 2100
4G RFM FRME 800
Single RAN Benefits :
Power savings: equipment, outdoor site
Lower rental costs
RF at mast: short feeders, improved RF performance
Re-use of Antenna System, power
Nokia Internal Use

## Slide 42
Opportunity to accelerate renewal with SRAN16
Example 2: Own Installed Base Modernization with SRAN
3G FSMD
4G FSMF
3G RFM FRGP 2100
4G RFM FRME 800
Existing Site
GSM 900/ 1800 4+4+4/ 4+4+4
WCDMA 2100 2+2+2@20W
LTE 800 1+1+1 @ 10MHz
2G FSMF
2G/ 3G/ 4G FSMF+ 2 FBBC
2G/4G RFM FXED 1800
2G/3G RFM FXDB 900
3G RFM FRGP 2100
4G RFM FRME 800
Modernized site GSM 900/ 1800 3+3+3/ 4+4+4
WCDMA 2100 2+2+2@20W + WCDMA 900 1+1+1
LTE 800 1+1+1 @ 10MHz + LTE 1800 @ 10 MHz
Reused modules
New modules
Nokia Internal Use

## Slide 43
Example SRAN 16.10: looking for configuration alternatives (2G&3G&4G)
SRAN 2G/3G/4G (RFM: 1xFXCB + 1x FXFC + 3x FRIG + 1xFRPB)
FSMF
FBBA/C
FBBA/C
2G&3G
1x FXCB (850MHz,3x80W)
3G: 222 @20W
*2G: 333@15W
2G&3G
1x FXFC
(1900MHz,3x80W)
3G: 222 @20W
*2G: 333@15W
4G
3x FRIG
(AWS,2T4R)
4G: 1+1+1, @20MHZ/40W
FSMF
FBBA/C
FBBA/C
WCDMA(only) dual band
Option 1: One SRAN BTS with two FSMF – not supported for this configuration request
Option 2: SRAN BTS and dedicated LTE BTS – supported
4G
1x FRPB
(APT700,2T2R)
4G: 1+1+1, @15MHZ/20W
* + MCPA Power Pooling
Confirmed SRAN (Y/N) | 
Option 1 | N
Option 2 | y
RRH supported in SRAN16.10, RF Modules supported in SRAN16.2
Nokia Internal Use

## Slide 44
GSM Modernization with LTE introduction
Legacy GSM BTS
TRS
TRS
Pre Modernization
900/1800
2100
FSMD
Baseband
Example from an Indian Customer
Post Modernization : Ph.2
Common TRS
900
1800
2100
SM Sharing
FSMF+FBBC
LTE introduction with Legacy GSM Modernization

## Slide 45
Gradual network evolution to Single RAN model
Gradual Network Evolution
SBTS Sites (MutliRAT sites using SBTS SW)
SBTS Sites (Single RAT GSM/WCDMA/LTE Mode using SBTS SW)
Eth
IP / Ethernet
Existing Transport
(TDM / IP)
Radio Controllers
RAT Specific Sites (FSMF or earlier system modules, RAT specific SW
mcBSC, Flexi BSC, mcRNC
  Mixed SBTS Deployments on Multi RAT and Single RAT sites
    SBTSs running on SRAN SW in Multi RAT or Single RAT mode (GSM / WCDMA / LTE)
  Single RAT sites with RAT specific SW
    SBTS and RAT Specific cites can be connected to same RNC/BSC. This requires the controllers to be upgraded to level where the BSCs and RNCs support SRAN e.g. GSM 16 & WCDMA 16 for SRAN16.10 or GSM17 & WCDMA17 for SRAN17
  Single RAT areas can stay on separate SW release levels as long as these are supported by the NetAct release in use

## Slide 46
Nokia Unique Selling Points: SRAN Value Adding Functionalities
RF sharing
Solution
Key functionality
Nokia unique selling points
  Common use of RF equipment between technologies
  Supported by Flexi Multiradio RF modules since 2008
  3 and 6-pipe RFMs, 4T4R RRH
High Value Feature examples
  SBTS Channel Bandwidth, Energy Efficient Coverage, MCPA Power Pooling
Liquid SW suite
  High Value Features to enable major improvement in capacity where needed
  Wide portfolio for most dynamic Radio Access features available
  Smart LTE Layering, Mass Event Handler, Application Aware RAN, Fast Dormancy Profiling, OSC, DFCA, Energy Efficient Coverage, Smart Dual Beam
Traffic steering
  Directing the traffic to most optimum technology layer
  Deep experience in complicated multivendor cases and references in KPI improvement
  Multi-band Load Balancing, Measurement Based HO, CSFB to UTRAN or GSM, Smart LTE HO, Smart LTE Layering, Fast Return to LTE
Transport
  Connectivity from BTS
  Integrated solutions for Nokia equipment
  QoS Aware Ethernet Switching, Synchronization Hub, Packet Abis over IP, Synchronous Ethernet
Re-farming
  Effective spectrum re-use for mobile broadband
  Highest spectrum efficiency with quality KPIs maintained, reference cases
  DFCA, OSC, Smart Dual Beam, Carrier Bandwidth, Dual Cell, Flexible UL Bandwidth
Security
  Transport security
  Integrated solutions for Nokia equipment
  IP Security features, IPSec Emergency Bypass, Secure File Transfer, A5/3 Ciphering
Site Solutions
  Multi-purpose site solutions for minimized TCO
  Simpler sites with 3 sector RF modules
  Same System Module for all radios (FSMF)
  From siteless to heavy macro integrations
  6-Sector Solution, RAS Vertical Sectorization, Composite MultiSite Transmission, Local Switching
Common O&M and SON
  Automation for efficiency in complex networks
  Common NetAct for RATs, references
  Common BTS OAM for single BTS SW upgrades
  CM auditing, CM history
  Automated Neighbor Relation, BTS Auto-connectivity

## Slide 47
1
2
3
4
5
6
7
8
Executive Summary
Single RAN
Portfolio
Customer
Benefits
Sales Guidance
Pricing
CI
References
Contacts

## Slide 48
Choosing the right SW and System Module HW for your deployments
Single RAN sales guidance
Software Selection
Hardware Selection
Dedicated RAT SW
To be offered if majority of your customer configs. or features are not supported with SBTS SW
Please remember: SBTS and dedicated RAT SW can be deployed simultaneously in same/different controller areas
FSMF System Module
Standard offering for dedicated GSM or WCDMA deployments
Standard SRAN offering until SRAN 17A system release
For low to medium capacity SRAN sites even after SRAN 17A release
SRAN SW
Offer SBTS if majority of your required configurations are covered with SBTS
Check configuration details in Sales Guidance Section
AirScale System Module, SRAN 17A
For high or very capacity LTE/ SRAN sites, 3 or 4-RAT sharing with TDD-LTE
Refer to config. details in ”Sales Guidance” section
Common CPRI for selected fALU LTE Radios in SRAN configurations

## Slide 49
Nokia System Module selection
SBTS SM hardware
Single FSMF configurations
Single common unit configurations
Flexi Multiradio 10 System Module
Dual common unit configurations
Dual FSMF configurations
AirScale System Module
SBTS software
RF Sharing
Backhaul Sharing
S1/X2
Iub
PAbis
IP
System Module Sharing
GWL
Fronthaul Sharing
G
W
L
OBSAI
Common BTS OAM
Common UI
Single logical SBTS
SRAN support in SRAN 17A
Nokia Internal Use

## Slide 50
What System Module should be offered?
Main categories | Sub-categories | Flexi Multiradio 10 System Module **) | AirScale System Module
Distributed RAN – Single-RAT BTS | GSM or WCDMA |  | 
 | LTE, up to 3 cells *) |  | 
 | LTE, 4-6 cells *) |  | 
 | LTE, more than 6 cells *) |  | 
Distributed RAN – SRAN BTS (2-4 RATs) | SRAN with GSM & WCDMA up to 15.5 SU***) |  | 
 | SRAN with GSM & WCDMA more than 15.5 SU***) |  | 
 | SRAN with LTE, up to 6 cells *) |  | 
 | SRAN with LTE, more than 6 cells *) |  | 
Centralized RAN |  |  | 
*) @20 MHz 2x2 MIMO equivalents (both FDD and TD-LTE);
**) for TD-LTE 4x4 and 8x8 MIMO use cases with Flexi Multiradio 10: Indoor variant is a better choice than Outdoor
***) 16 SU is approx. equivalent 18 carriers with 45 voice users, 45 HSPA users.
Offer AirScale when
When full FSMF (FSMF+2x extension cards) required for LTE
More than 2xFSMF (w/o extensions) required until SRAN17A. When full FSMF (FSMF+2x extension cards) required after SRAN17A.
Technical requirements like LTE4.5Pro or 5G readiness requires always AirScale
Nokia Internal Use

## Slide 51
SRAN use Case and capacity definition for FSMF and AirScale SMs
Typical deployment in a Distributed network architecture
Ideal for building SRAN coverage and basic capacity
Typical deployment: 2-3 band MultiRAT sites
Optimized for outdoor deployments
Can be deployed in a Distributed or Centralized network architecture requiring capacity baseband pool
Optimized for high capacity LTE/SRAN deployments
Default option for 3-RAT deployments with 4x4 MIMO
LTE4.5Pro, 5G future evolution
Flexi Multiradio 10 System Module
AirScale System Module
Min capacity with one FSMF
1-RAT or 2-RAT(G/L, G/W)
Typical capacity with extensions
2 to 3-RAT site with G/W, G/L Sharing
LTE 2x2MIMO in 2 layers
Typical capacity (1 to 3 -RAT)
Low WCDMA utilization, FDD LTE 4x4 MIMO at high FDD bands, 2x2 MIMO at low FDD bands
Typical capacity (3-RAT)
High WCDMA utilization, FDD LTE 4x4 MIMO at high FDD bands, 2x2 MIMO at low FDD bands

## Slide 52
Typical SRAN deployment scenarios
Very high capacity D-RAN
6+ bands, 4 RATs
Coverage D-RAN
1-2 low frequency bands
All outdoor site
High capacity D-RAN
4-5 bands
Basic capacity D-RAN
1-3 bands
/
    AirScale or FSMF
    FSMF
    AirScale
    D-RAN = Distributed RAN. System Module on each site

## Slide 53
SRAN System Module Positioning Table for Single RAN Sites
Configuration type | Typical/exemplary configuration | FSMF | AirScale System Module
Coverage | Coverage 2 bands, LTE 2x2 MIMO | Recommended | 
Basic capacity | Basic capacity 3 bands, LTE 2x2 MIMO | Recommended | Recommended if capacity evolution or 4x4 MIMO is foreseen in near future
High Capacity | High Capacity 3 to 5 bands, LTE 4x4 MIMO at high bands, 2x2 MIMO at low bands |  | Recommended
Very High Capacity | Very high capacity Up to 7 bands, FDD LTE 4x4 MIMO at high FDD bands, 2x2 MIMO at low FDD bands TD-LTE 8x8 MIMO future expansion |  | Recommended
Flexi MR 10 System Module should be the default offering for Single RAT sites and for Basic Capacity SRAN Sites
AirScale system Module is a Premium Product and should be offered mainly for :
  High Capacity Single RAN Sites
  Sites with 3-RAT and TD-LTE Baseband Sharing
  Sites Requiring Common CPRI with fALU LTE Radios
  LTE4.5Pro or 5G as a mandatory requirement
  AirScale radio unit support
Nokia Internal Use

## Slide 54
Future evolution
Options for outdoor sites
2-8 Plug-in units in 7U Outdoor Subrack
2-4 Plug-in units in 4U Outdoor Subrack
Basic Capacity Outdoor subrack (AMOC)
From low to high capacity configurations
Distributed RAN
Installation in outdoor conditions without any additional protection
High Capacity Outdoor subrack (AMOB)
From low to very high capacity configurations
Distributed RAN
Installation in outdoor conditions without any additional protection
Full resiliency support
1-3 capacity sub-modules in 3U
Flexi Multiradio 10
Ideal for basic SRAN coverage and medium capacity
Installation in outdoor conditions without any additional protection

## Slide 55
SBTS Support for Radio Modules
(MRS Mode)
SRAN17A and onwards
FSMF and AirScale System Module
Always check the latest available material using the below link.
https://intranet.nokia.com/global/work/marketing/portfolio/mbbsalesportal/singleran/pages/sran17.aspx
SRAN17 Tab  sales guides and technical documentation  SBTS supported RF configurations (PPT)

## Slide 56
850
1800
FXDB(3T6R)
3x80W
FHDB(2T2R)
2x60W
900/900J
FXEB(3T6R)
3x80W
FXED(6T6R)
6x60W
FXEE(3T6R)
3x80W
FHEB(2T2R)
2x60W
FXEF(3T6R)
3x80W
FHEL(2T2R)
2x60W
SRAN17A
FHEF(2T2R)
2x60W
Tx Rx
Rx
GSM
WCDMA
LTE
3 RAT simultaneous Sharing based on configuration request
FXDA(3T6R)
3x60W
FHDA(2T2R)
2x40W
FXEA(3T6R)
3x60W
FHEA(2T2R)
2x40W
3Gbps OBSAI
6Gbps OBSAI
FXCB(3T6R)
3x80W
FXCA(3T6R)
3x60W
FXDD(6T6R)
6x60W
9.8Gbps CPRI
SRAN18/SRAN18A
FHDI(2T2R)
2x60W
FXDJ(3T6R)
3x60W
FXJB(3T6R)
3x80W
FRCG(2T2R)
2x60W
Nokia Internal Use
AHDA(2T4R)
2x60W
AHDB(2T4R)
2x60W
AHEB(4T4R)
4x40W
AHED(2T4R)
2x80W
AHEC(2T4R)
2x80W
FHED(4T4R)
4x40W

## Slide 57
1900
2100
FXFC(3T6R)
3x80W
Tx Rx
Rx
GSM
WCDMA
LTE
FXFA(3T6R)
3x60W
FXFB(3T6R)
3x60W
3Gbps OBSAI
6Gbps OBSAI
FRGT(3T6R)
3x80W
FRGY(2T2R)
2x60W
FRGU(6T6R)
6x60W
FRGS(3T6R)
3x80W
FRGX(3T6R)
3x80W
FRGB(2T2R)
2x60W
FRGP(3T6R)
3x60W
FRGQ(2T2R)
2x40W
1.7/2.1
FRIJ (4T4R)
4x40W
9.8Gbps CPRI
FHGA(2T2R)
2x5W
3 RAT simultaneous Sharing based on configuration request
AHGA(2T4R)
2x60W
SRAN17A
SRAN18/SRAN18A
Nokia Internal Use
FHFB(4T4R)
4x40W

## Slide 58
Dual Band
(1800/2100)
Dual Band
(1900*/
AWS(1.7/2.1))
Tx Rx
Rx
GSM
WCDMA
LTE
3Gbps OBSAI
6Gbps OBSAI
AHEGA(2T4R)
2x120W
AHPMDA(2T2R)
2x120W
9.8Gbps CPRI
* 3 RAT simultaneous Sharing based on configuration request
Triple Band
(700/800/900*)
AHEGB(4T4R)
2x4x40W
AHFIB(4T4R)
2x4x40W
SRAN17A
SRAN18/SRAN18A
Nokia Internal Use

## Slide 59
From SRAN profiles to cell sets
Improved BTS configuration concept

## Slide 60
From profiles to cell sets
99.9
Fixed configurations described by profiles
Profile defines configuration on BTS level
Profiles have (too) detailed information about the maximum system module HW, radio HW setup, OBSAI cabling, baseband allocations, RAT multiplexing rules in the fiber.
Therefore even small configuration changes require new profile
  Means additional test effort, often even coding effort.
  Limited number of configurations released, while hundreds are needed.
  Higher effort on site migration from legacy RAT to SRAN
SBTS Configuration „Cell Set” approach:
Cell sets defined on sub-baseband module level are combined as independent building blocks to build an SBTS configuration
System module – Radio Module connection topology is auto detected. Commissioning rules, Baseband allocation and data routing are calculated based on detected topology.
LTE cell sets to be supported in SBTS
New SRAN cell sets for shared operation (LTE-WCDMA, LTE-GSM, GSM-WCDMA) and dedicated RAT operation for GSM and WCDMA are defined.
LTE and SRAN cell sets can be flexibly combined to build target configuration.
SRAN 16.x
SRAN 17.x onwards

## Slide 61
What configurations are supported?
Why do we need cell sets
Nokia to publish supported configurations that are described by sub-configurations called „cell sets”
Customer, based on published cell sets ia able to plan BTS configuration and connect HW (RF and SM) accordingly
BTS during first start-up detects RF on specific ports, Customer creates carrier configuration and assigns to detected RF HW.
BTS (DCS) calculate RAT allocation to BB, IQ data routing, etc.
BTS capacity and performance are at the level described by cell sets. BTS is OnAir.
Cell sets is a way to describe supported configurations towards customer
Customer plans and dimensions configurations based on the cell sets provided by Nokia
Cell sets are described on sub-baseband level and can be combined together to achieve full configuration.
There is no direct indication about particular cell sets in the SW code
SW has to provide capacity and performance at least as it is described by the cell sets

## Slide 62
LTE
Cell Set based Configurations in SRAN 17A: more configurations per SRAN release
99.9
Profiles are replaced by Cell Set approach for both AirScale and FSMF System Modules:
Cell sets defined on sub-baseband module level are combined as independent building blocks to build an SBTS configuration
Testing and releasing is done on cell-set level
System module – Radio Module connection topology is auto detected. Commissioning rules, Baseband allocation and data routing are calculated based on detected topology.
LTE and SRAN cell sets can be flexibly combined
LTE
ASIA
LTE
WCDMA
Future expansion
Future expansion
Future expansion
Future expansion
Current LTE Cell Sets
GSM
New SRAN Cell Sets
SRAN Cell Set
LTE cell sets:
  LTE configurations from LTE SW will be supported in SRAN 17
  Part of SRAN17A parity with LTE
SRAN cell sets:
  GSM, WCDMA, RAT sharing (LTE-GSM, WCDMA- GSM, LTE-WCDMA)

## Slide 63
SBTS
configuration
LTE and SRAN cell sets
SBTS configurations
LTE cell set N
SRAN cell set N
Compatibility level of SRAN and LTE cell sets
BB cell set
RF set 1
+
RF set n
+…+
Full BTS level
Cell set level
LTE cell set X
SRAN cell set X
LTE cell set Y
LTE cell set Y
LTE cell set X
…
SRAN cell set X
SRAN cell set Y
…
Cell sets are defined in such a way that they describe sub-configurations, which are independent from each other
Testing and releasing happens on cell set level
These cell sets can be combined in various ways, like Lego blocks.
This flexibility with cell sets allows higher number of configurations per SRAN release
Cell Set - description of building blocks:
LTE cell sets
  Pure LTE configurations from LTE SW to be supported in SRAN as part of parity with LTE
SRAN cell sets:
  GSM, WCDMA, RAT shared building blocks (LTE-GSM, WCDMA- GSM, LTE-WCDMA)

## Slide 64
SRAN profiles vs SRAN cell set concept with sample spectrum
SRAN16:
BTS profiles – predefined BTS configuration:
BTS level configuration definition
HW
Cabling
BB allocation
Cell amount
Antenna Configuration type
800 | 900 | 1800 | 2100 | 2600
2xFRMA 1xFRMC 3xFRMB | 2xFXDB GSM 2xFXDB 2T2R@LTE-GSM 2xFXDB 2T4R@LTE-GSM 3xFHDB2T2R@LTE-GSM 2xFXDB 2T4R@LTE-GSM | 1xFXED 2T2R@LTE 2xFXED 4T4R@LTE 3xFHED 2T2R@LTE 3xFHED 4T4R@LTE | 1xFRGU 3xFRGY | 2xFRHA 1xFRHC 3xFRHB 3xFRHG
3x5x4x2x4 = 480 profiles
SRAN17:
Cell sets - description of building blocks:
LTE cell sets:
  Pure LTE configurations from LTE SW to be supported in SRAN 17
  Part of SRAN17 parity with LTE
SRAN cell sets:
  GSM, WCDMA, RAT shared building blocks (LTE-GSM, WCDMA- GSM, LTE-WCDMA
3+4+4 = 11 LTE cell sets
5+2 = 7 SRAN cell sets

## Slide 65
SRAN Feature Parity

## Slide 66
SRAN Release Content
SRAN
Releases
Single BTS OAM, AirScale BB, IoT
Parity with LTE17A, GSM17, WCDMA17
High Capacity SRAN deployments with AirScale Radios and Baseband
  AirScale SM support (3-RAT)
  4-RAT site solution including TD-LTE
  Outdoor sub-rack AMOB
Narrow Band IoT, CAT-M
New Radios : FXDD, FHDI, FHGA
GSM: 36TRX, MOBSS, MCPA Power pooling, Extended cell range
Improved Account Management
BTS Mediator Resiliency
RF sharing and chaining
Extended sync capabilities
New AirScale Radios and site solutions
AirScale RF evolution
  Higher iBW, Multiband Radios
  Single Band Radios : AHEB, AHED, AHDB
  Multi Band Radios: AHEGA, AHEGB, AHFIB. AHMPDA
Parity with LTE, WCDMA and GSM releases
X2 mesh Connectivity
SRAN Lean GSM Solution
SBTS Nokia CPRI Chaining and Sharing
FDD/TDD CA-support for SBTS with 2x FSMF
Inter-site carrier aggregation
Latest LTE IoT features
SRAN 17A
SRAN 18
SRAN 18A
Harmonized Radio OAM platform
Latest RAT features (G/W/L)
TDLTE support in SRAN
AirScale and FSMF Chaining
MSR PIM Cancellation for AirScale Radios
Support for New AirScale Radios
New BB Platform support
BTSMED Support for BTS Plug and Play
Dynamic Spectrum Sharing
Remote Mass migration from Single RAT to Single RAN
5G interworking

## Slide 67
SRAN 17A Release Highlights
AirScale Base Station Support
New AirScale System Module
Higher Capacity Single RAN sites
3-RAT capability (GSM, WCDMA, FDD-LTE) in one system module
4-RAT site solution to enable TD-LTE
Outdoor sub-rack AMOB/ Indoor AMIA
New AirScale Radio Units
6T/6R Radio in 900 band (FXDD)
2T/2R Radio in 900J band (FHDI)
Low power Radios (LTE/WCDMA) (FHGA)
Site Solution Evolution
New configurations with flexible SRAN cell set approach
OBSAI RF Sharing and Chaining
Support for selected fALU LTE Radios
Inter-eNB CA SBTS(FDD) – LBTS(TD)
MORAN/MOCN/MOBSS support
36 GSM TRXs
GSM extended cell range
    IoT/M2M communication
    NB-IoT In-band support
    LTE-M support
Operability evolution
Single BTS O&M unified architecture
New BTS Mediator with resiliency
Common Web Element Manager
Dedicated RAT to SBTS Migration
Remote ALDs SW Mngt
Transport and Security
    Dynamic X2 and S1 Firewall configs
    Fronthaul Passive/Active WDM
    Extended synchronization capabilities
Enhanced security access control
Efficient transport of Small IP packets
    Latest RAT features
    LTE-FDD 17A, WCDMA 17, GSM 17

## Slide 68
SRAN 18 Release Highlights
Site Solution Evolution
Additional configurations with flexible SRAN cell set approach
Lean GSM opening up new refarming possibilities
New AirScale Radio Units
RRH 4T4R B3 160W AHEB
RRH 4T4R B66 160W FRIJ
RRH 2T4R B3 160W AHED
RRH 2T4R B8 120W AHDB
Dual RRH 2T4R B1/3 240W AHEGA
Dual RRH 4T4R B1/3 320W AHEGB
Dual RRH 4T4R B25/B66 320W AHFIB
Tri RRH 2T2R B8/20/28 240W AHPMDA
    IoT/M2M communication
    NB-IoT Standalone
    Loose Phase and Time Synchronization
Transport and Security
    X2 Mesh connectivity with IPsec
    Latest RAT features
    GSM 18
    WCDMA 18
    LTE-FDD 18

## Slide 69
RAT Feature Parity Plan in SRAN Releases
Radio Resource Management / Telecom and selected other features
RAT | SRAN 16.10 | SRAN 17A | SRAN 18 | SRAN 18A
GSM | SRAN 16.2 supported GSM features Additional GSM feature parity introduced DFCA features1 Phase sync for DFCA1 Flexible MCPA TX Power Pooling Energy efficient coverage | GSM 17 level features Available via new SBTS O&M features MOCN/MOBSS 36 TRXs support Extended Cell support | GSM 18 level features Available via new SBTS O&M features CMST Satellite Abis | GSM 18 level features Available via new SBTS O&M features Smart Dual Beam
WCDMA | SRAN 16.2 supported WCDMA features | WCDMA 17 level Features Available via new SBTS O&M features MOCN/MORAN Efficient transport for Small IP packets | WCDMA 18 level Features | WCDMA 18 level Features
LTE | SRAN 16.2 supported FDD-LTE features | FDD-LTE 16A and FDD-LTE 17A level Features Available via own SBTS O&M features MORAN/MOCN In-band NB-IoT Cat-M fALU RFs support Additional FDD-LTE feature parity Inter eNB TDD-FDD CA | FDD-LTE 18 level Features Available via own SBTS O&M features Inter eNB RF sharing | FDD-LTE 18A level Features Available via own SBTS O&M features LTE MBMS
For details in SRAN 16.2 1.0 feature and functionality restrictions, please refer to Impact Document in NOLS Software Supply Tool.
1 SRAN 16.10 1.0
Nokia Internal Use

## Slide 70
SRAN17A feature parity
Feature ID | SRAN17A Exclusion Feature Component Title
LTE2483 | Classical WCDMA/LTE RF-sharing on AirScale SM Indoor
LTE2881 | Support of classical WCDMA/LTE RF-sharing on 3Tx/6Rx RF-module (Rel. 3.3-family)
LTE2998 | 4- and 6-sector support for classical WCDMA/LTE RF-sharing
LTE3129 | Classical WCDMA/LTE RF-sharing with 40 MHz occupied bandwidth
LTE3688 | Additional FDD-TDD Carrier Aggregation band combinations - V
LTE3778 | User throughput to include the Initial Burst Delay
RAN1273 | HSPA Pre-emption for NRT-over-NRT
RAN3353 | Online management of MHA
RAN3354 | Online management of Antenna Line Devices
RAN3358 | OMS for Nokia CBIS
RAN3107 | RF sharing with RF unit chaining
RAN3331 | WCDMA-support for RF-sharing with LTE AirScale
RG302513 | Non-GSM BTS SW upgrade with GSM BTS EM
RG602507 | Automatic output power adjustment for Multi-Carrier configurations
  Link to: RAT Feature parity with SBTS –material :
Nokia Internal Use

## Slide 71
1
2
3
4
5
6
7
8
Executive Summary
Single RAN
Portfolio
Customer
Benefits
Sales Guidance
Pricing
CI
References
Contacts

## Slide 72
Capacity
SBTS Data User (WCDMA, LTE)
Data Volume GB
Busy Hour Throughput Mbps
WCDMA R99 CE
Single RAN SBTS
Pricing for SRAN introduces new triggers
Essential Pack (2G, 3G, LTE SW Releases)
Price per SRAN Cell
ASW
Price per SRAN Cell, per SBTS and per share
Capacity/HWA
Price per R99CE, TRX, SBTS Data User, Data Volume, Busy Hour Throughput, Channel Bandwidth (HWA), Watts
HW
HWA
ASW
Capacity
Users, Throughput
New Features, Release
BW, Power
Nodes, Cells
Monetization Triggers Growth Levers
ASW
Essential Pack
SM-Module Sharing
RF-Module sharing
Multi-RAT operation
Others
HWA
GSM TRX
Channel bandwidth
Incremental Power

## Slide 73
  Max number of Data Users connected per SRAN SBTS during the measured time
  Data User counts WCDMA and LTE Data users including LTE VoLTE users
    GSM users and WCDMA R99 voice excluded
  Following data user states included
    LTE Connected UE (secondary cell coming later)
    WCDMA HSDPA and HSUPA users in Cell DCH or (High Speed) Cell FACH state
  Data User license is freely configurable with 1 data user steps
  Data Users only in SRAN SBTS because trigger includes both LTE and WCDMA users
SBTS Data User
  Data Volume is linked to an operator’s revenue stream and not to e.g. network elements
  Measured on SBTS level, charged on Network level
  SBTS Data Volume measurement is technology agnostic
    No separation between LTE , WCDMA or GSM
  Data Volume introduction in SRAN SBTS and LTE
SBTS Data Volume
  Busy Hour Throughput is an option for Data Volume
  Measured on SBTS level, charged on Network level
  SBTS Busy Hour Throughput measurement is technology agnostic
    No separation between LTE , WCDMA or GSM
  SBTS Busy Hour Throughput introduction in SRAN SBTS
    also usable capacity trigger for all Single RATs as the trigger counts all traffic coming through SBTS.
    If SBTS is in e.g. WCDMA-only mode, all busy hour throughput traffic is WCDMA related
SBTS Busy Hour Throughput
SRAN Pricing: New SBTS capacity triggers

## Slide 74
  Channel Bandwidth is an essential new HW Activation trigger as it captures both used bandwidth and number of cells under one SI
    Easy to understand as both bandwidth and cells are commonly understood among operators
    Gives good upsell when networks grow
  Channel Bandwidth is configured per SRAN SBTS
  Channel Bandwidth counts activated bandwidths and cells per WCDMA , LTE and bandwidth and TRXs on GSM
  Mandatory SI per SRAN BTS
    Channel Bandwidth is HW Activation license
SBTS Channel Bandwidth
  Measured and priced in 1MHz steps
  Channel Bandwidth per RAT
    LTE BW: 20MHz, 15MHz, 10MHz, 5MHz, 3MHz, 1.4MHz
    WCDMA: 5MHz
    GSM: 200kHz
  Cell definition with Channel Bandwidth is the same for all RATs
    1+1+1 equals 3 Cells
    2+2+2 equals 6 Cells
    2+2+2 MIMO equals 6 Cells
    Etc.
  Channel Bandwidth introduction in SRAN SBTS
SRAN Pricing: New HW Activation
  Examples
    LTE 111@20MHz = (3 cells x 20MHz) x 1MHz license =60 licenses
    LTE 111@10MHz = (3 cells x 10MHz) x 1 MHz license = 30 licenses
    LTE 222@20MHz = ( 6 cells x 20MHz) x 1 MHz license = 120 licenses
    WCDMA 222 = (6 cells x 5MHz) x 1MHz license = 30 licenses
    GSM 222 = (6 TRXs x 200kHz) x 1MHz license = 1 license
  Number of required licenses is rounded down to the closest integer (example 5 above)
  Investment’s value not vanishing over the coming years
    Even if # of e.g. # of WCDMA Cells decreases, licenses are available for LTE

## Slide 75
SRAN configuration tool for preparing SW offer

## Slide 76
    SI: SR00100LK SBTS RF Module HW Sharing RLK (License controlled)
    SI: SR00100.T SBTS RF Module sharing LTU (SWAM controlled)
    SI: RL000094.T RF-Sharing LTE - GSM LTU
    SI: RL000123.T RF-Sharing LTE - WCDMA LTE
    SI: RAN1770C.T RF-Sharing WCDMA – GSM
    SI: SR001015LK SBTS Incremental Power RTU (License controlled)
    SI: SR001015.T SBTS Incremental Power LTU (SWAM controlled)
    SI: BSC00548 GSM BTS Power License 20W Step
    SI: RAN2225.T 20W incremental power license
    SI: RL000144.T 20W Incremental Power extension
  Single RAT
  20W Power
  Single RAN
SRAN Pricing: SBTS SI and license mapping table
    SI: BSC00311 TRX HW Activation license
    SI: RAN2123.4T WCDMA R99 CE
    SI: RAN2123.2T HSDPA Processing Set 2
    SI: RAN2123.3T HSDPA Processing Set 3
    SI: RAN2123.5T HSUPA Processing Set
    SI: RAN2123.6T CCCH Processing Set
    SI: RL000042.T LTE Connected UE
    SI: RL000148.T LTE Throughput capacity DL
    SI: RL000149.T LTE Throughput capacity UL
  Capacity
    SI: BSC00311 TRX HW Activation License
    SI: RAN2123.4T WCDMA R99 CE
    SI: RAN2123.6T CCCH Processing Set
    SI: SR001004.T SBTS Data User
    SI: SR000384.1.T SBTS Daily UP Data Volume
    SI: SR000384.3.T SBTS Quarterly UP Data Volume
    SI: SR000384.2.T SBTS Busy Hour UP Throughput
RF-Sharing
    SI: SR001005.T SBTS Channel Bandwidth
    SI: RAN1001.T Flexi WCDMA BTS Multi-Carrier
    SI: RAN3017.T Additional 6 WCDMA cell activation
    SI: RAN2964 Flexi WCDMA BTS 6-sector solution
    SI: RL000049.T Cell Bandwidth 1,4MHz
    SI: RL000048.T Cell Bandwidth 3MHz
    SI: RL000026.T Cell Bandwidth 5MHz
    SI: RL000027.T Cell Bandwidth 10MHz
    SI: RL000047.T Cell Bandwidth 15MHz
    SI: RL000028.T Cell Bandwidth 20MHz
  BTS Site

## Slide 77
SRAN data volume is the sum of LTE and WCDMA data volume
Data Volume dimensioning allows TCO calculation with realistic scenario
Understanding WCDMA Data volumes - today
  Examples of WCDMA customers BTS:
    Highest capacity sites > 100 GB daily
    Average capacity sites ~ 26 GB per day
    Low capacity sites <2 GB per day
  On Network level
  1-31,500 TB monthly
   1-94,500 TB quarterly
Understanding of LTE Data volumes - today
  Examples of LTE customers eNodeBs:
  Highest capacity sites: >500 GB daily
  Average capacity sites: 100 GB daily
  Low capacity sites: <10 GB daily
  On Network level
  1-12,000 TB monthly
   1-36,000 TB quarterly
  Data volume per user varies as well
  Heavy LTE users: ~10-20 GB per month
  Av. LTE users: ~1-5 GB per month
Existing data volume usage varies a lot

## Slide 78
Performance Benchmarker KPIs for Data Volume
Available from NetAct measurements or MINT/Performance Benchmarker
Current data traffic is a good reference for existing Nokia customers
  Get operator specific, current Data traffic load by using measurements
    LTE
      PDCP SDU Volume UL per day (M8012C19)
      PDCP SDU Volume DL per day (M8012C20)
      Number of active eNBs
    WCDMA
      HSUPA Data Volume per day(M1023C10 )
      HSDPA Data Volume per day (M5000C126)
      Number of active WBTSs
    GSM
      GPRS UL Payload data
      GPRS DL Payload data
      EGPRS UL Payload data
      EGPRS DL Payload data
Data Volume counters
LTE
    LTE: PDCP SDU Volume DL per day (LTE_5212)
    LTE: PDCP SDU Volume UL per day (LTE_5213)
WCDMA
    HSDPA Data Volume per day (RNC_608)
    HSUPA Data Volume per day (RNC_931)
GSM:
    GSM: GPRS UL Payload Data (TRF_212)
    GSM: GPRS DL Payload Data (TRF_213)
    GSM: EGPRS UL Payload Data (TRF_214)
    GSM: EGPRS DL payload data (TRF_215)
Note: Performance Benchmarker KPIs provide a reference but will not be identical to SWAM numbers due to 14 day averaging. In urban sites the variance is in the range of some percents, in remote sites e.g. in business areas this can be tens of percents.
Nokia Internal Use

## Slide 79
  SBTS Capacity triggers will be used in Greenfield SRAN cases
  Data volume and Busy Hour Throughput capacity triggers can be used also directly with Single RAT BTS
    Data Volume and Busy Hour Throughput measure the total IP traffic volume or BH Throughput and are therefore directly usable also on Single RAT mode
    Data Volume trigger for dedicated LTE (available since 2015) has different SI than SRAN
    WCDMA voice with R99 CE and GSM with TRX(HWA)
  SBTS Data User is not directly usable for Single RAT case because it is based on total number of WCDMA and LTE Data Users (taken into account also in IRP price)
Greenfield case
Typical case having both SBTS and single RAT BTS
  Typical case is where operator has single RAT sites and Single RAN sites at the same time
  Parallel SBTS and Single RAT capacity models possible
  There might be pressure to convert all sites to support the same capacity pricing model
  Conversions require careful planning because wrong pricing can jeopardize monetization
  SBTS Capacity triggers include existing GSM TRX and WCDMA R99CE
    No conversion needed
  Conversion needed with
    WCDMA Processing Set
    LTE Connected UE and UL/DL Throughput
Single RAN SBTS Capacity trigger deployment

## Slide 80
SM-Module Sharing customer pricing
  SM-Sharing: n/a
  SBTS Multi-RAT Operation: n/a
  SM-Sharing: n/a
  SBTS Multi-RAT Operation: x1
  SM-Sharing: n/a
  SBTS Multi-RAT Operation: x1
  SM-Sharing: x1
  SBTS Multi-RAT Operation: x1
  SM-Sharing: x1
  SBTS Multi-RAT Operation: x1
  SM-Sharing: x1
  SBTS Multi-RAT Operation: x1
  SM-Sharing: x1
  SBTS Multi-RAT Operation: x1
  SM-Sharing: x1
  SBTS Multi-RAT Operation: x1
  SM-Sharing fee will be charged when more than one RAT shares the same plug-in unit (IRP/share)
  SBTS Multi-RAT Operation feature is needed when 2 or more RATs in the same SBTS (IRP/SBTS)

## Slide 81
Single RAN ASW pricing
Single RAN ASW feature pricing
      Single RAN ASW pricing model follows Single RAT model
      Single RAN ASW is priced per SRAN Cells or SBTS
      Separation to SDT (Standard) and HVF (High Value Features) categories based on the value
      SDT features activated normally to all Cells but HVF only on need bases
    Definition of Single RAN Cell
      Single RAN Cell counts all cells on GSM, WCDMA and LTE side where functionality is activated
      Note: Simplified method, to convert GSM TRXs, if no other approach => GSM 3+3+3 =3 cells GSM 5+5+5=5 cells
      Etc.
WCDMA
3 Cells
6 Cells
9 Cells
+
=
LTE
3 Cells
3 Cells
6 Cells
SRAN
9 Cells
12 Cells
18 Cells
Definition of Single RAN Cell
GSM
3 Cells
3 Cells
3 Cells
+
WCDMA
1
3
2
LTE
1
3
2
SRAN
3
2
5
1
4
6

## Slide 82
SRAN Release Upgrade Pricing
  First SRAN release, SRAN16.2, is called and priced as SRAN Essential Pack.
  Next SRAN releases will be sold as Release Upgrades.
  SRAN Release Upgrade includes, with few exceptions*
    GSM Release
    WCDMA Release
    FDD-LTE Release
    SRAN specific functionalities
      *Exceptions are described in Feature parity material
  TDD-LTE will be part of coming SRAN releases
  SRAN Release Upgrade has a price € / SRAN Cell
    SRAN Cell counts all activated cells (GSM, WCDMA and LTE cells)
    The price includes SRAN specific Basic SW functionalities and valuable features
  Next SRAN Releases are an upgrade on top of Essential Pack. When existing GSM/WCDMA/ LTE are upgraded to SRAN NW, the following upgrades are needed: SRAN Essential Pack (€/SRAN Cell) + GSMxx RU (€/TRX) + WCDMAxx RU (€/cell) + FDD-LTExx RU (€/cell)
  Operators pay for single RAT RUs which they activate as SRAN

## Slide 83
RAT[Rel.16]
RAT[Rel.17]
SRAN17A
RAT[Rel.17]
SRAN16.xx
Conversion to SRAN
Conversion to SRAN
SRAN RU
RAT RU
1. Operator has ”older level” N-1 Single RAT releases: GSM 16, WCDMA 16, LTE 17
  Step 1: Single RAT release upgrade to GSM17, WCDMA17, LTE17A
  Step 2: Conversion to SRAN 17A (conversion pricing: EUR 200/ SRAN cell)
2. Operator has ”same level ” N Single RAT Rel.17: GSM 17, WCDMA 17, LTE 17A
Step 1: Converson to SRAN 17A (conversion pricing: EUR 200/ SRAN cell)
3. Operator has SRAN 16.xx
Step 1: Release upgrade to SRAN 17A (SRAN RU pricing: EUR 600/ SRAN cell)
RAT = LTE / WCDMA / GSM
3 options for pricing steps
1
2
3
Pricing options for SRAN 17A Release Upgrade
Nokia Internal Use

## Slide 84
Scenarios: SRAN configurations Pricing SRAN Case: SRAN and/or SRAN conversion => SRAN [N+1]
The scenarios are based on 3-RAT configuration: Source: SRAN Sales Playbook v.4.1
GSM 24 TRXs
WCDMA 10 cells
LTE 3 cells @20MHz 2x2 MIMO equivalent
WCDMA&LTE
WCDMA
GSM&WCDMA
LTE
3- RAT GSM&WCDMA&LTE
Case 2a: WCDMA/GSM/LTE are below N+1
=> Needed upgrades:
WCDMA/GSM/LTE to N+1
SRAN conversion
Case 2b: SRAN in level N
=> Needed upgrades:
SRAN to N+1

## Slide 85
1
2
3
4
5
6
7
8
Executive Summary
Single RAN
Portfolio
Customer
Benefits
Sales Guidance
Pricing
CI
References
Contacts

## Slide 86
Single RAN key differentiators |  |  |  |  |  | 
Single RAN capable hardware |  |  |  | x |  | x
Unique six-pipe RF Module world leading macro site compactness |  | x | x | x | x | x
High capacity 3RAT outdoor baseband IP65 protected casing, zero-footprint, high-capacity |  |  (low capacity variant) | (Assumed w/RBS6303) | x | x | x
Unique advanced spectral efficiency features Liquid Radio SW suites are re-farming enablers, field proven in heavy traffic networks |  | (VAMOS) | (VAMOS) | x | x | x
Energy efficient base station 3RAT BB sharing, RFM, EE SW features |  |  (low capacity variant) | (Assumed w/RBS6303) | x | (cabinet cooling) | x
Synchronized SW releases Single RAN functionality across 2G/3G/4G |  |  |  | x | x | x
Modular SingleRAN controller for GSM and WCDMA 80% same HW, re-purposing from GSM to WCDMA possible |  |  (not modular) |  (not modular) | x | x | x
Nokia Single RAN differentiators Positive effect on power consumption and OPEX

## Slide 87
Single RAN key differentiators |  |  |  | 
SM sharing with Outdoor baseband 3RAT with single module, no cabinet with cooling needed |  |  (low capacity variant) | (Assumed w/RBS6303) | x
RF sharing 6 pipe RFM, 3RAT sharing supported by platform |  | No 6 pipe, 3RAT supported by platform | No 6 pipe, 3RAT supported by platform | No 6 pipe, 3RAT supported by platform
Common BTS OAM Single SBTS SW, Single logical BTS, remote BTS SW upgrade to SBTS SW |  | x | x | x
Fronthaul sharing 3RAT supported, capacity 80MHz @ 6Gbps |  |  |  | x
FDD/TDD-LTE unique features Frequency Selective Scheduler (FSS) |  | x |  | x
WCDMA unique features Mass event handling |  |  |  | x
GSM unique features DFCA, SRA, EC-EGPRS |  | No SRA, one IBCA reference, EC-EGPRS | x | x
Nokia SRAN17 release differentiators

## Slide 88
Nokia 2x2 MIMO site with only 1 RF module - Only vendor with a 6-pipe radio
Nokia
1x Radio module 6-pipe 240/360W
Huawei
3x Blade RRU
Ericsson
3x Radio System RRU (2016)
Samsung
3x SRU

## Slide 89
3RAT configuration, example
3 LTE cells 20MHz, and
9 WCDMA cells, and
12 GSM TRX’s
RF connectivity up to 12 ports
Nokia 3RAT outdoor baseband - unique
LTE or WCDMA
Eri Radio System has only indoor BB
3 RAT
LTE/GSM or WCDMA/GSM
GSM not confirmed
Only one BBU PIU due to limited cooling
6 LTE cells 20MHz, or
6 WCDMA cells, possibly
64 GSM TRX’s
RF connectivity 6 ports
Nokia
FSMF with 2xFBBA/C and SBTS Software in SRAN16.2
Ericsson
RBS6302, WCDMA SW 4Q2012, LTE SW 2Q2013
Huawei
BBU3900 with OMB cabinet and UMPT, UBBPd_U and L
Huawei Blade BBU
BBU3910A3
6 LTE cells 20MHz
RF connectivity 6 ports
WCDMA & LTE are different variants
LTE
not seen in field
Nokia Internal Use

## Slide 90
Flexi BTS feederless site vs. Ericsson- 3 band example
Superior site solution with Flexi BTS
3- sectors
3 x bands
MIMO
RF sharing
Flexi RFM
6 TX/MIMO, 6x60W
3 TX, 3x80W
2 x RFM stack
1 x RFM
1 more can be added on same plinth
Traditional RRUs
Highest distance 10-20m from antenna
Flexi BTS site solution
Less space needed
Less installation
Less site rent
Less wind load
Less weight
Easier installation
Space left for antennas
Space left for site evolution
Space left for tower & site sharing with other operators
More output power available
Better performance
More power for RF sharing
10 years field proven including OD baseband

## Slide 91
Flexi BTS feederless site vs. Huawei- 3 band example
Superior site solution with Flexi BTS
2 x RFM stack
Flexi BTS site solution
Less space needed
Less installation
Less site rent
Less wind load
Less weight
Easier installation
Space left for antennas
Space left for site evolution
Space left for tower & site sharing with other operators
More output power available
Better performance
More power for RF sharing
10 years field proven including OD baseband
1 x Band
3 x Blade RRU
2x60W 1800 (fat- blade)
2x40W other bands (blade)
3- sectors
3 x bands
MIMO
RF sharing
Flexi RFM
6 TX/MIMO, 6x60W
3 TX, 3x80W
1 x RFM
1 more can be added on same plinth

## Slide 92
Energy efficiency is one of key Nokia strengths
Win deals -> Smart tendering
Offer latest hardware variants and energy efficiency SW
Use figures measured according to ETSI 102 706 stardard
Make sure customer uses comparable figures, e.g. same traffic load, RF output power and number of TX pipes
Remind customer that competitors products may need cooling and they may offer figures obtained only with certain software features
Case Elisa Finland learnings
Huawei attacked with new LTE energy efficiency story
Nokia Rel2 HW measured against Huawei new Blade RRU & new LTE energy saving features (designed for Huawei)
Huawei 50% better in low LTE load conditions
Huawei cooling system was not included in measurement
Nokia obtained sole supplier status after succesfull fight:
  Energy efficiency workshops
  Offer with latest 6-pipe RFM and promise of LTE SW EE products
  Existing RF modules supporting RF-sharing - no new RF needed
Best hardware
Power prioritizer
No cooling needed
Nokia FSMF and RFM
Measured ETSI 102 706
Best LTE/WCDMA SW with
Micro DTX
MIMO muting
Layer switch off
Best SRAN and GSM BTS SW
3RAT SM and RF sharing
Integrated backhaul transport
GSM energy efficiency
Slow Drain Voltage Modulation (SDVM) planned to LTE/WCDMA 17 releases
Leading energy measurement
Power metering & Eden-NET energy management
Unique Zero Emission 2.0
Nokia journey to better world - decouple traffic and CO2
Internal sales guidance

## Slide 93
1
2
3
4
5
6
7
8
Executive Summary
Single RAN
Portfolio
Customer
Benefits
Sales Guidance
Pricing
CI
References
Contacts

## Slide 94
64 SRAN Release Customer References
Nokia Internal Use

## Slide 95
Public Single RAN Customer References *
Nokia Internal Use
* Source: http://www.nokia.com/en_int/news/releases

## Slide 96
Strong Nokia Single RAN Advanced deal momentum continues
Recent deals
TIM, is the first operator in Brazil to use the 2600 MHz and refarm the 1800 Mhz frequency band to 4G LTE. TIM is now ready to make the move to future-proofing its network using the 700 MHz spectrum band.
Bharti Airtel will deploy its 4G FDD-LTE & TD-LTE technology, expand 3G network and modernize 2G BTS. The rollout uses Nokia's radio access with Single RAN technology for FDD-LTE and TD-LTE
China Mobile sign EUR 1.36 billion frame agreement including AirScale Base Station
Three Ireland sign five-year contract to simplify and upgrade radio access network operations
Zain KSA boost 4G network speeds aggregating 25 MHz of spectrum on 900 MHz, 1800 MHz and 2100 MHz bands
Ooredoo Qatar sign three-year network expansion agreement on 2G, 3G, 4G LTE, LTE-Advanced radio and core technologies
3Sweden will upgrade it network with TD-LTE-Advanced radio technology, based on the Flexi Multiradio 10 Base Station, to support 2600 MHz band 38 WCDMA and FDD-LTE network upgrade Care Services
Korea Telecom conduct world’s first LTE-M (eMTC) field trial with Flexi Multiradio 10 Base Station
Ooredoo Qatar boost network up to 375 Mbps with LTE-A three-band carrier aggregation on 800/1800/2600 MHz
http://networks.nokia.com/news-events/press/press-releases
Nokia Internal Use

## Slide 97: Nokia Single RAN Advanced Customer References
  337 customers with Single RAN Advanced products
  288 customers with multiple radios from Nokia
  120 Zero Emission customers
  64 Single RAN Release customers
97
© Nokia 2017
Nokia Internal Use

## Slide 98
337 Nokia Single RAN Advanced Customer References
Nokia Internal Use
In 105 countries

## Slide 99
Radio deliveries in numbers
LTE
WCDMA
Two radios
GSM
Three radios
Multiple radios from Nokia
305
279
366
138
176
288
One radio
267
Nokia Internal Use

## Slide 100
1
2
3
4
5
6
7
8
Executive Summary
Single RAN
Portfolio
Customer
Benefits
Sales Guidance
Pricing
CI
References
Contacts

## Slide 101
For latest roadmap communication
SRAN Roadmap
Latest Roadmap
Latest future and understudy features
https://nokia.sharepoint.com/sites/RoadmapCommunity/Mobile%20Networks%20BG%20Roadmaps/Forms/AllItems.aspx

## Slide 102
For more information
SRAN17A Sales & Marketing portal
Key messages & contacts
Customer presentations
Roadmaps
References
Competitor Intelligence
SRAN Playbook
Links to useful content
https://nokia.sharepoint.com/sites/SingleRAN/SRAN17A/SitePages/Home.aspx

## Slide 103
For more information
SW Material Portal
SW Release Sales Materials
HVF/E-HVF Sales Pack
SW Bundles Materials
Available for all RATs
https://nokia.sharepoint.com/sites/SWSales/Lists/SW%20Material%20Portal1/AllItems.aspx#InplviewHash7b93b440-7992-4446-853b-0b4874c1f306=FilterField1%3DProduct-FilterValue1%3DSRAN

## Slide 104
For more information
Content Store – Single RAN Collection
Find the information fast
Latest collaterals
Most wanted information
Links to useful content
https://workspaces.int.nokia.com/sites/mcacs/Pages/Main_Angular.aspx#/CollectionDetailview/Documents/None/None/None/None/None/None/None/None/None/None/None/None/None/None/None/None/None/None/156

## Slide 105
For more information
nokia.com
Our story for public
Tell to your customer
Video (1,5 min)
White Paper
Executive Summary
Product pages
https://networks.nokia.com/products/single-ran-advanced

## Slide 106
For more information
Key Single RAN contacts
Contacts: | Contacts:
Harry Kuosa Marketing harry.kuosa@nokia.com | Yrjö Koskinen / Petri Rantala War Room yrjo.koskinen@nokia.com / Petri.Rantala@Nokia.com
Majid Ektesabi Software Sales majid.ektesabi@nokia.com | Kaia Ostonen Portfolio Sales kaia.ostonen@nokia.com
Bernd Bradter Release Product Manager for SRAN16.2 and SRAN18 bernd.bradter@nokia.com | Mariusz Korzepa Release Product Manager for SRAN16.10 and SRAN 17A mariusz.korzepa@nokia.com
Nishant Gautam Head of SRAN Business Product Management nishant.gautam@nokia.com | 

## Slide 108
Revision History
Document Owner: Majid Ektesabi Reviewers & contributors: Nishant Gautam, Petri Rantala, Majid Ektesabi, Harry Kuosa, Kaia Ostonen, Andreas Ringhandt, Ireneusz Jany, Frank Beismann, Andrzej Polak, Mariusz Korzepa ---------------------------------------------------------------------------------------------------------------------------------------------------- |  |  |  |  | 
Version | Description of charges | Date | Handled by | Status | Approver
1.0 | First approved version | 02.04.2014 | Jari Malinen | Approved | Nishant Gautam
2.0 | Rebranding, modernization topic enhanced, pricing & other minor updates | 04.07.2014 | Jari Malinen | Approved | Nishant Gautam
3.0 | Introduction of SRAN16, SBTS, War-room Modernization Learning's, New SBTS price licensing regime included along with minor updates | 31.03.2015 | Ashvinder Chopra | Approved | Nishant Gautam
4.0 | Updated with SRAN 16.2 contents | 01.10.2015 | Aniruddha Bose, Anish Roy | Approved | Nishant Gautam
4.1 | Updated after review, pricing principles | 27.11.2015 | Petri Rantala | Approved | Nishant Gautam
5.0 | SRAN 16.10 and SRAN 17 updates, Sales guidance | 31.07.2016 | Petri Rantala/Nishant Gautam | Approved | Nishant Gautam
6.0 | SRAN17 updates | 19.12.2016 | Majid Ektesabi | Approved | Nishant Gautam
7.0 | SRAN17A Updates | 03.11.2017 | Majid Ektesabi | Under review | 

## Slide 109
Copyright and Nokia Internal Useity
The contents of this document are proprietary and Nokia Internal Use property of Nokia. This document is provided subject to Nokia Internal Useity obligations of the applicable agreement(s).
This document is intended for use of Nokia’s customers and collaborators only for the purpose for which this document is submitted by Nokia. No part of this document may be reproduced or made available to the public or to any third party in any form or means without the prior written permission of Nokia. This document is to be used by properly trained professional personnel. Any use of the contents in this document is limited strictly to the use(s) specifically created in the applicable agreement(s) under which the document is submitted. The user of this document may voluntarily provide suggestions, comments or other feedback to Nokia in respect of the contents of this document ("Feedback"). Such Feedback may be used in Nokia products and related specifications or other documentation. Accordingly, if the user of this document gives Nokia Feedback on the contents of this document, Nokia may freely use, disclose, reproduce, license, distribute and otherwise commercialize the feedback in any Nokia product, technology, service, specification or other documentation.
Nokia operates a policy of ongoing development. Nokia reserves the right to make changes and improvements to any of the products and/or services described in this document or withdraw this document at any time without prior notice.
The contents of this document are provided "as is". Except as required by applicable law, no warranties of any kind, either express or implied, including, but not limited to, the implied warranties of merchantability and fitness for a particular purpose, are made in relation to the accuracy, reliability or contents of this document. NOKIA SHALL NOT BE RESPONSIBLE IN ANY EVENT FOR ERRORS IN THIS DOCUMENT or for any loss of data or income or any special, incidental, consequential, indirect or direct damages howsoever caused, that might arise from the use of this document or any contents of this document.
This document and the product(s) it describes are protected by copyright according to the applicable laws.
Nokia is a registered trademark of Nokia Corporation. Other product and company names mentioned herein may be trademarks or trade names of their respective owners.